## Slide 1: BlueDBM : An Application for Big Data Analytics
Presented By: Nitin Mukesh Tiwari
Instructor : Dr. Akhilesh Tyagi
Some of the material is taken from original presentation of MIT research group

## Slide 2: Authors
Sang- Woo Jun Ming Liu
Sungjin Lee Jamey Hicks
John Ankcorn Myron King
Shuotao Xu Arvind
Presented at: ISCA’ 2015 (The 42nd International Symposium on Computer Architecture )

## Slide 3: Big Data Revolution
Analysis of data at large scale can give important insights.
Google predicted Flu out breaks before CDC.
Nate Silver predicted US presidential election results with 100% accuracy using Twitter Data.
Amazon is planning anticipatory shipping of products based on Big Data
etc …
Biggest economic driver for IT industry in future

## Slide 4: RamClouds- popular solution for Big Data
Cluster of machine with large DRAM capacity and fast inter connect
  Fastest in in terms of execution time.
  Very Costly and Power hungry
  Performance of system falls sharply even with small fraction of references to secondary memory
What if Data does not fit in DRAM ??

## Slide 5: Proposed Solution
Flash based memory
  Faster than disk and cheaper than DRAM
  Relatively low power consumption
  Legacy storage systems are burdening
  Slower than DRAM

## Slide 6: Related Work
Flash Memory
  SSDs, PCIe enabled SSD, SanDisk ZetaScale
  Moneta, NoFtl
Networks
  Faster network fabrics like Infiniband, RDMA, User Level TCP stack, QuickSAN
Accelerator
  In-store processing, Smart SSD, Ibex, XSD

## Slide 7: BlueDBM
BlueDBM
Flash Based Storage
Low latency high throughput inter controller network
In Store Processing capability

## Slide 8: BlueDBM Overall System Architecture
Homogeneous cluster of host servers
BlueDBM is plugged in Host

## Slide 9: BlueDBM Node Architecture
Each Node contains:
In-store processing capability
Host Interface
Flash interface
Network Interface

## Slide 10: BlueDBM node architecture
In-Storage
Processor
Flash
Controller
Network
Interface
Host Server
Flash Device
PCIe
Lightweight flash management with very low overhead
  Adds almost no latency
  ECC support
Custom network protocol with low latency/high bandwidth
  x4 20Gbps links at 0.5us latency
  Virtual channels with flow control
Software has very low level access to flash storage
  High level information can be used for low level management
  FTL implemented inside file system
Flash
Controller
Network
Interface
Host Server
Notes: All three components involve a lot of engineering and ideas and there is just no time to present everything in detail.
We will try to publish multiple publications regarding each of these components, or we can talk about details separately after the talk.

## Slide 11: Flash Interface
A low-level thin and Fast hardware interface which:
  Minimizes the access latency from network or in store processors
  Exposes all degree of parallelism of device
Writes and Reads Data in 128 bit bursts

## Slide 12: Network Interface
Low latency High bandwidth network infrastructure across all BlueDBM storage
Enables a flexible and configurable topologies among storage eg. Distributed start
Contains: Logical End Points, Link layer and Routing layer

## Slide 13
Simple Token based flow control
Back pressure ensures the packets are not dropped.
Deterministic Routing Optional end-to-end protocol support

## Slide 14: Host Interface
In store processor can be accessed by Host interface which works on RPC
Read and Write have 128 page buffers each.
Uses DMA to parallelize read and write.
  Parallelizing read is tricky as data is read in 128 bit burst.

## Slide 16: Software Interface
Flash system interface
  Complete FTL implementation
  RFS like implementation for better performance
Block Driver Interface
Accelerator interface

## Slide 17: BlueDBM software view
Block Device Driver
Connectal (By Quanta)
Flash Ctrl
NAND Flash
File System
Accelerator Manager
BlueDBM provides a generic file system interface as well as an accelerator-specific interface (Aided by Connectal)
Hardware-assisted Applications
Kernel-
space
FPGA
User-
space
HW Accelerator
Network
Interface

## Slide 18: Latency in Distributed Flash-based Analytics
Distributed processing involves:
  Flash Device Access
  Storage Software
  Network
  Actual Processing
Flash
Access
75 μs
50~100 μs
Storage
Software
100 μs
100~1000 μs
Network
20 μs
20~1000 μs
Processing
…
Latency is additive

## Slide 19: Latency in distributed flash-based analytics
100~1000 μs
Storage
Software
100 μs
Architectural modifications can remove unnecessary overhead
  Near-storage processing
  Cross-layer optimization of flash management software*
  Dedicated storage area network
  Accelerator
Flash
Access
75 μs
50~100 μs
Network
20 μs
20~1000 μs
Processing
…
< 20μs
…
Notes: Latency is additive because data needs to be copied to and from DRAM

## Slide 20: Power consumption is low
Component | Power (Watts)
VC707 | 30
Flash Board (x2) | 10
Storage Device Total | 40
Component | Power (Watts)
Storage Device | 40
Xeon Server | 200+
Node Total | 240+
Storage device power consumption
is a very conservative estimate
GPU-based accelerator will double the power
Notes: 20%

## Slide 21: Application Example: Graph traversal
Very latency-bound problem, because often cannot predict the next node to visit
  Beneficial to reduce latency by moving computation closer to data
Flash 1
Flash 2
Flash 3
Host 1
Host 3
In-Store Processor
Host 2
Notes:   Benefits of lower latency access into distributed flash for computation on large graphs

## Slide 22: Other potential applications
Genomics
Deep machine learning
Complex graph analytics
Platform acceleration
  Spark, MATLAB, SciDB, …

## Slide 23: Conclusion
Fast flash-based distributed storage systems with low-latency random access may be a good platform to support complex queries on Big Data
Reducing access latency for distributed storage require architectural modifications, including in-storage processors and fast storage networks
Flash-based analytics hold a lot of promise, and we plan to continue demonstrating more application acceleration

## Slide 24: Near-Data Accelerator is Preferable
DRAM
Motherboard
CPU
DRAM
Flash
NIC
Accelerator
FPGA
CPU
Flash
NIC
Motherboard
Accelerator
FPGA
CPU
DRAM
Flash
NIC
FPGA
Motherboard
CPU
DRAM
Flash
NIC
FPGA
Motherboard
Hardware & software latencies are additive
BlueDBM
Traditional Approach

## Slide 25: References
BlueDBM: An Appliance for Big Data Analytics
people.csail.mit.edu/

## Slide 26
Thank you